## Slide 1
S4 / S12 • FINAL PROJECT
DESIGN & SIMULATION OF A
4-BIT BINARY
ARITHMETIC CALCULATOR
A digital-logic circuit for binary arithmetic using switches, gates and adders.
TEAM MEMBERS
E. Yashwanth Chowdary — 2620030377
K. Teja Sri Hamsini — 2620030382
K. Guna Nandini — 2620030427
E. Lokesh Kumar — 2620030368
Section: S4 / S12
01 / 06

## Slide 2
01 • OVERVIEW
Introduction & Objective
02 / 06
DIGITAL LOGIC • FINAL PROJECT
A compact calculator that represents numbers in binary and performs arithmetic through digital logic.
WHAT IS 4-BIT?
Four binary digits; each bit is 0 or 1. Unsigned range: 0–15.
PROJECT OBJECTIVE
Design, simulate and test a 4-bit arithmetic circuit in Logisim Evolution.
EXPECTED OUTPUT
Binary result bits, with carry/borrow status where supported.
PROJECT FLOW
01
Inputs
→
02
Logic
→
03
Arithmetic
→
04
Outputs
Note: a 4-bit result can overflow the 0–15 range; the carry-out is useful to observe.

## Slide 3
02 • FUNDAMENTALS
Theory & Logic Circuit
03 / 06
DIGITAL LOGIC • FINAL PROJECT
Binary place values
8
2³
4
2²
2
2¹
1
2⁰
Core gates
AND
OR
NOT
XOR
AND: both 1 • OR: at least one 1 • NOT: invert • XOR: inputs differ
4-bit adder block diagram
A[3:0]
B[3:0]
4-BIT ADDER
SUM[3:0]
CARRY OUT
Each full-adder stage adds Aᵢ, Bᵢ and the carry from the previous stage.
S = A ⊕ B ⊕ Cᵢ | Cₒ = AB + ACᵢ + BCᵢ

## Slide 4
03 • IMPLEMENTATION
Circuit Design in Logisim Evolution
04 / 06
DIGITAL LOGIC • FINAL PROJECT
Implementation overview
1
Place inputs
Use 4-bit input pins or four switches for A and B.
2
Build arithmetic
Use a 4-bit adder or connect four full-adder stages.
3
Connect outputs
Attach sum bits and carry-out to output pins/LEDs.
4
Test inputs
Change A and B and verify the displayed result.
LOGISIM WORKSPACE (SCHEMATIC)
A[3:0] = 0101
B[3:0] = 0011
4-BIT
ADDER
SUM = 1000
Illustrative block diagram — replace this panel with your actual Logisim screenshot before submission.
If subtraction is included, use a mode control and two's-complement logic (B ⊕ SUB, carry-in = SUB).

## Slide 5
04 • VALIDATION
Simulation Results
05 / 06
DIGITAL LOGIC • FINAL PROJECT
Example test cases for a 4-bit unsigned adder
A
B
A + B
Carry
Expected result
0000
0000
0
0
0000
0001
0001
2
0
0010
0101
0011
8
0
1000
0111
0001
8
0
1000
1111
0001
16
1
0000 + carry
WORKED RESULT
0101
+ 0011
──────
1000
5 + 3 = 8
Truth table note
A complete truth table for a 4-bit adder has 2⁸ = 256 input combinations (four bits for A and four for B). The table above is a concise set of representative tests, not the complete truth table.
Replace the illustrative result panel with a real screenshot from your Logisim simulation.

## Slide 6
05 • WRAP-UP
Conclusion & Applications
06 / 06
DIGITAL LOGIC • FINAL PROJECT
WHAT WE ACHIEVED
• Represented unsigned values using four binary bits.
• Applied logic-gate and adder principles to arithmetic.
• Outlined a Logisim simulation and representative verification tests.
• Observed why carry-out matters when results exceed 15.
APPLICATIONS
CPU / ALU
Arithmetic and logic operations
Embedded systems
Small digital control and processing circuits
Education
Learning combinational logic and simulation
Future improvement
Add/subtract mode, overflow flag, display and more operations
FINAL TAKEAWAY
A small 4-bit circuit demonstrates the same binary arithmetic principles used inside larger digital systems.
TEAM: Yashwanth Chowdary • Teja Sri Hamsini • Guna Nandini • Lokesh Kumar